# Task:	Descents and Descending Turns

Definition:	A basic maneuver used to reduce altitude while descending or gliding on a constant heading or turning.

Objective:	To develop student skill in maneuvering the airplane after reaching cruising altitude and on approach.  Develops student understanding of skill in: effect and use of flight controls; management of attitude and power to control performance; and use of trim; all while using outside references to the horizon.  Maneuver is a building block; directly related to normal landing procedures.

When:

Where:

Preflight Discussion:

- Effect and use of flight controls.

- Elevator controls pitch by decreasing down force.

- Change attitude using pressure on elevator control.

- Recommended glide speed maintained by reducing power setting and adjusting pitch as necessary to maintain glide speed.

- Visual references for pitch, roll and yaw.

- Nose slightly below horizon  - have student note exact sight picture when correct attitude established.

- Wings equally below horizon.

- Proper rate of turn for descending turns.

- Exact sight picture of standard rate turn.

- Sight picture will vary from left and right.

- Ground references to maintain constant heading.

- Instrument references for pitch, roll and yaw.

- Nose slightly below horizon bar on A/I – have student note exact sight picture when correct attitude established.

- Wings level in relation to horizon bar on A/I.

- Note T/C for proper rate of turn on descending turns – standard rate and verify ball is centered.

- For descents without turns, verify T/C needle is centered.

- Note A/S/I to maintain glide speed – increase/decrease pitch as necessary to maintain.

- Note H/I to check constant heading.

- Establish descent from level cruise flight.

- Apply carb heat.

- Reduce power.

- Use back elevator pressure to hold altitude constant until the airspeed decreases to recommended glide speed.

- Decrease pitch attitude – release back elevator pressure – to maintain glide speed.

- As airspeed stabilizes, retrim for “hands-off flight”.

- More forward elevator pressure  will be required for descending turns than straight descents as turns reduce glide performance.

- Use rudder to coordinate turns.

- Turn entry

- Exiting turn

- Cross check and correct attitude as necessary.

- Level off

- Rear elevator pressure to increase pitch to level flight attitude.

- Lead by at least 50-100 ft. (for 500 fpm, lead by 100-150 ft.)

- When descent altitude approaches, apply back elevator pressure, increase power as necessary to maintain airspeed.

- Carb heat cold.

- Roll out of descending turns to headings solely by reference to H/I – lead roll out on H/I by ½ bank angle.

- Trim to relieve control pressure when airspeed is stabilized.

- Trim technique

- Trim used to relieve control pressure.

- Trim maintains an airspeed (angle of attack), not an altitude.

Instructor Demonstration:

- Establish descent attitude, power and trim.

- Have student describe attitude sight picture when established.

- Have student describe use of carb heat.

- Have student describe power setting used.

- Have student describe torque correction.

- Have student describe trim technique.

- Level off

- Have student describe attitude sight picture when established.

- Have student describe power setting used.

- Have student describe carb heat cold.

- Have student describe torque correction.

- Have student describe trim technique.

Student Practice:

- Use integrated technique (IR then VR or VR then IR).

- Use verbal correction – avoid control inputs.

- Have student explain actions during initial performance.

- Watch for errors – correct immediately.

- Attitude control

- Control input sequence – power, pitch, trim.

- Inadequate cross check of outside references and instruments.

- Over concentration on pitch – neglecting roll and yaw.

- Improper trim technique

- Failure to wait for airspeed to stabilize.

- Not fully relieving control pressure.

- Tenseness and overcontrolling

- Improper trim technique – death grip on wheel.

- Moving controls rather than applying pressures.

- Improper turn coordination on turning climbs – ball to left or right.

- Turn entry

- Exiting turn

e.  Failure to use carb heat.

- Review performance

- Save critique until performance complete.

- Have student repeat as necessary.

Evaluation:

- Airspeed within +/- 10 knots (Private).

- Heading constant within +/- 20 degrees.

- Altitude within +/- 200 feet.

- Smooth coordinated use of flight controls and power.

- Proper integrated approach; use of both visual references and instrument cross checks.