# Task:	Straight and Level Flight

Definition:	Maintain the airplane on a constant altitude and heading.

Objective:	To develop student skill in maintaining the airplane on a constant altitude and heading.  Develops student understanding of skill in: effect and use of flight controls; Integrated Flight Instruction method, trim technique and methods to overcome tenseness and over-controlling; all while using outside references to the horizon.

When:

Where:

Preflight Discussion:

- Effect and use of flight controls.

- Ailerons neutral.

- Throttle to cruise setting.

- Elevator pressure neutralized for minimal gain/loss in altitude.

- Visual references for  roll, pitch and yaw.

- Nose reference to horizon  - have student note exact sight picture when correct attitude established for straight and level flight.

- Wing tip positions in relation to the horizon, equal on both sides.

- Instrument references for pitch, roll and yaw.

- Nose upon horizon bar on A/I – have student note exact sight picture when correct attitude established.

- Wings straight and level – even with the  horizon bar on A/I.

- Note T/C needle should be straight up and down

- Note H/I to check for intended heading.

- Trim technique

- Trim used to relieve control pressure.

- Trim maintains an airspeed (angle of attack), not an altitude.

Instructor Demonstration:

- Establish straight and level flight and trim.

- Have student describe attitude sight picture when established.

- Have student describe power setting used (cruise setting).

- Have student explain instruments used for crosscheck.

- Have student describe trim technique.

Student Practice:

- Use integrated technique (IR then VR or VR then IR).

- Use verbal correction – avoid control inputs.

- Have student explain actions during initial performance.

- Watch for errors – correct immediately.

- Attitude control

- Control input sequence – ailerons, rudder and pitch.

- Inadequate cross check.

- Improper trim technique

- Not fully relieving control pressure.

- Most common error if student can’t hold altitude.

- Tenseness and over-controlling

- Improper trim technique – death grip on wheel.

- Moving controls rather than applying pressures.

d. Review performance

- Save critique until performance complete.

- Have student repeat as necessary.

Evaluation:

- Airspeed within +/- 10 knots.

- Heading constant within +/- 20 degrees.

- Altitude within +/- 200 feet.

- Smooth coordinated use of flight controls and power.

- Proper integrated approach; use of both visual references and instrument cross-checks.